## Slide 1: Partial reconfiguration on IOT device
Android on zynq featuring updateable FPGA-accellerated image processing and hashing
Ing. Andreas Dejmek, BSc
Christoph Grafl
Florian Muttenthaler, BSc
Benedikt Tutzer, BSc
Institute of Computer Technology
TU Wien

## Slide 2: Project
Zedboard: Xilinx Zynq developement board
  Android OS
  Output over HDMI
  Input from USB-Touchscreen
Image processing app with programmable-logic accelerated algorithms
Server to retrieve updates to accelerators
programmable-logic hashing to verify the received bitstream
Dynamic partial reconfiguration of the programmable-logic

## Slide 3: Android on Zynq
Issues with Android:
  Hardware requirements for versions after android 2.3.7 not met
  Older versions require out-of-date toolchain versions that are hard to find
  Official repository shut down
Solutions:
  Build on Ubuntu 12.04 (from 2012)
  Use the cross-compiling toolchain from Xilinx ISE 14.4 (from 2012)
  Use fork on github by use aimeemikaelac
  ANDROID NOW BOOTING ON ZEDBOARD!

## Slide 4: Android on Zynq
Issues with custom Logic on the Zedboard
  Reference Design out of date. Builds neither with current tools nor with tools from 2012
  Cannot create custom Bitstream
  u-boot requires tools not available in Ubuntu 12.04
Solutions:
  Zynq zcu102 development board?
  Build using Xilinx ISE 14.4, but with some IP cores from Xilinx ISE 14.1
  Build some tools (make, device-tree-compiler) from source
  CUSTOM BITSTREAM GENERATED AND WORKING

## Slide 5: Android on Zynq
Status:
  Android Booting
    Internet: working (With manual dhcp enabling)
    Touchscreen: not working
  Can read/write registers on FPGA from Android
Next Steps:
  Implement Protocol to interface FPGA Logic
  Implement Linux kernel extension
  Include Blake2b hashing entity

## Slide 6: Image Filters

## Slide 7: Image Filters
Using Xilinx Platform Studio for creating 3 different IPs with common AXI Interface
Implemented Linux Kernel Device Driver, which writes and reads raw ARGB Data from a .bin file and triggers the filter processes

## Slide 8: Data Streaming
Filters are stored on a server and made accessible to client devices
Server
Stores and distribute bitstreams
Python 3, Flask
RESTful API
Create-Read-Update-Delete(CRUD)
Client
Native android app
Poll server periodically
Download bitstream
Reconfigure fabric

## Slide 9: Data Streaming
Server-Client communication over HTTP
RESTful Server API:
HTTP GET /api/repos/soc_lab
Return all information about repo ‚soc_lab‘
HTTP POST /api/repos/another_soc_lab_repo + Data
Create a new repo ‚another_soc_lab_repo‘
HTTP PUT /api/repos/soc_lab + Data
Create or update a repo ‚soc_lab‘
HTTP DELETE /api/repos/soc_lab
Delete repo ‚soc_lab‘

## Slide 10: Data Streaming
Client polls server for information
http:// … /api/soc_lab
Server returns relevant information from Database(version,changelog,filepath…)
Client compares his version with server version
Download bitstream, if not up to date
http:// … /api/download/<filepath>
Verify bitstream integrity
Match checksum
Reconfigure FPGA fabric

## Slide 11: Data Streaming
Client Architecture

## Slide 12: Data Streaming
Flow:
Activity configures Network Manager
Network Manager polls server for information
Received JSON File will be forwared to Msg Processor
Msg Processor retriev information from JSON file, compare bitstream version. Informs Activity if new bitstream is available.
Activity will initiate download through Network Manager.
Msg Processor check md5 from downloaded file
Save bitstream to disk
Fabric Manager forwards bitstream to ?OS?

## Slide 13: Data Streaming
Problems:
OS handles address allocation
Only access to virtual memory space

## Slide 14: Created simple PR project for Zedboard
Consists of one PR region with two modules
  LED shift left
  LED shift right
Bitstreams generated but not tested yet

## Slide 15: Partial reconfiguration
PR project flow (GUI based)

## Slide 16: Control PR – two approaches
Control over Android
Using xdevcfg library
  Supported in our Android version?
Load Bitstream from memory to PL over PCAP

## Slide 17: Control PR – two approaches
Control over IP core
Using Partial Reconfiguration Controller v1.2
Android trigger the start of reconfiguration
IP load Bitstream from memory to PL over ICAP

## Slide 18: FPGA fabric partitioning
Static portion
  Control for image processing
  Blake2b hash entity
  (IP core PR controller ?)
Dynamic portion
  Red filter
  Green filter
  Blue filter

## Slide 19: Thank you for your attention