## Slide 1
Partial reconfiguration on IOT device
Android on zynq featuring updateable FPGA-accellerated image processing and hashing
Ing. Andreas Dejmek, BSc
Christoph Grafl
Florian Muttenthaler, BSc
Benedikt Tutzer, BSc
Institute of Computer Technology
TU Wien
Notes: 1

## Slide 2
Project
Zedboard: Xilinx Zynq developement board
  Android OS
  Output over HDMI
  Input from USB-Touchscreen
Image processing app with programmable-logic accelerated algorithms
Server to retrieve updates to accelerators
programmable-logic hashing to verify the received bitstream
Dynamic partial reconfiguration of the programmable-logic

## Slide 3
Android on Zynq
Issues with Android:
  Hardware requirements for versions after android 2.3.7 not met
  Older versions require out-of-date toolchain versions that are hard to find
  Official repository shut down
Solutions:
  Build on Ubuntu 12.04 (from 2012)
  Use the cross-compiling toolchain from Xilinx ISE 14.4 (from 2012)
  Use fork on github by use aimeemikaelac
Notes: Hardware requirements not met:
ZedBoard only has 512mb RAM → Not enough (could be solved by using SWAP memory, but SWAP on SD-cards is very very slow)
No GPU. Even 2.3.7 is slow, people that got higher versions running (with SWAP memory) encountered unusable graphical user interfaces

## Slide 4
Android on Zynq
Issues with custom Logic on the Zedboard
  Reference Design out of date. Builds neither with current tools nor with tools from 2012
  Cannot create custom Bitstream
  u-boot requires tools not available in Ubuntu 12.04
Solutions:
  Build using Xilinx ISE 14.4, but with some IP cores from Xilinx ISE 14.1
  Build some tools (make, device-tree-compiler) from source
Notes: We could have designed our own hardware design in Vivado, but this was deemed to be too much work for the short time we had available, since it must be designed with Linux compatibility in mind and none of us had the background knowledge to do that
Tools required by u-boot: right device tree compiler (dtc) version
Make 3.81 is required to build android, since there are some syntax errors in it’s makefiles and 3.82+ versions are more restrictive and generate errors

## Slide 5
Final Software Setup
Linux Kernel Version 3.6 from Digilent
  Configured to support Android
  Configured to support Dynamic Partial Reconfiguration (DPR)
  Configured to support USB Touchscreens
Android 2.3.7 customized for ZedBoard by Iveia
  Distributed by aimeemikaelac
  No Touchscreen support
Android app to trigger DPR, hashing entity and image filters
Kernel Modules to interface Hardware Logic
Notes: Linux kernel can be configured with “make menuconfig”
Necessary configuration for Android found at https://elinux.org/Zedboard_Android
Necessary configuration for touchscreens is straight-forward
Iveia shut down their repositories for some reason
Touch issues: Touchscreen is detected fine by Linux, so no hardware incompatibility. Events are detected by android (android has a built-in getevent utility) but never dispatched to the GUI. The same happens with a mouse, which should be supported out-of-box. I tried to trace where the events are lost: They are enqueued by native code to be picked up by the dalvik virtual machine, but the VM never picks them up

## Slide 6
Image Filters

## Slide 7
Image Filters
Using Xilinx Platform Studio for creating 3 different IPs with common AXI Interface
Implemented Linux Kernel Device Driver, which writes and reads raw ARGB Data from a .bin file and triggers the filter processes

## Slide 8
Image Processing App
Server
Stores and distribute bitstreams
Python 3, Flask
Development server
RESTful API
Client
Native android app
Gingerbread 2.3.3 (API 10)
Interacts with server and hardware
Notes: The Image processing app splits into two parts.
An external server which provides the infrastructure to store and distribute bitstreams and the android app which interacts with the server and the hardware on the zedboard.
Server is written with python 3 and flask (a web development framework for python)
REST … Representational state transfer. Is a standardized programming architecture style for server – client communication

## Slide 9
Server
Server-Client communication over HTTP
RESTful Server API:
GET /api/soc_lab_iot
Return all information about repo ‚soc_lab_iot‘
POST /api/another_lab_repo + Data
Create a new repo ‚another_lab_repo‘
PUT /api/soc_lab_iot + Data
Create or update repo ‚soc_lab_iot‘
DELETE /api/soc_lab_iot
Delete repo ‚soc_lab_iot‘
Notes: methods to read, create, update or delet a repository from the server

## Slide 10
Server
Example repository entry:
{
"Index": "SOC-LAB-IOT",
"Title": "IOT Image Processing",
"Version": "002",
"Description": "",
"Changelog": ["3.11.2018 Primary release",
"4.11.2018 Bug fixing",
"6.11.2018 added stuff"],
"File": "filter_0_0_4.bin",
"Date": "6.11.2018",
"Checksum": "fdg851df……“
}
Notes: What information we save on the sever. (the Data from the previous slide)
Most importan for us is the index,version,file and checksum

## Slide 11
Client
Issues
API 10 outdated (currently 28)
Pre historic android
Android rapidly evolved since then
“standard” android classes/components not existent
Solution:
Build with API 25 for target API 10
With Android Support Libraries (backwards compatibility)
Client app supported on Gingerbread and above (>10)

## Slide 12
Client
Architecture
Notes: How the client architecture looks like. Tasks are divided into three classes.
The network manager who handles all network I/O operation
The message processor who unpacks and reads what the server returns
The fabric manager who handles all the programmable logic interaction
(The other classes are rather unimportant, but if someone ask. They care about multi threading, and the image pre processing)
Activity is the main entry for every android appliction ( like the main method in C)

## Slide 13
Client
Polls server for information
Compares bitstream version
Initiate new bitstream download (if out of date)
Verify bitstream integrity (hash calculation HW accelerated)
Reconfigure PL Fabric with the new bitstream
Hardware ready to use

## Slide 14
Client
Simple user interface to trigger the download and to apply filters on the image.

## Slide 15
Created simple PR project for Zedboard
Consists of one PR region with two modules
  LED shift left
  LED shift right
Bitstreams generated but not tested yet

## Slide 16
Partial reconfiguration
PR project flow (GUI based)

## Slide 17
Control PR – two approaches
Control over Android
Using xdevcfg library
  Supported in our Android version?
Load Bitstream from memory to PL over PCAP

## Slide 18
Control PR – two approaches
Control over IP core
Using Partial Reconfiguration Controller v1.2
Android trigger the start of reconfiguration
IP load Bitstream from memory to PL over ICAP

## Slide 19
FPGA fabric partitioning
Static portion
  Control for image processing
  Blake2b hash entity
  (IP core PR controller ?)
Dynamic portion
  Red filter
  Green filter
  Blue filter

## Slide 20
Thank you for your attention